## Slide 1: Final Project Hardware Implementation of Pipelined MIPS and RISC-V
Speaker: Kane
Instructor: 吳安宇教授
Date: 2021/05/20
Digital System Design

## Slide 2: MIPS/RISC-V Processors
Single-Cycle
  Simple design with low throughput
Pipelined
  Higher throughput
  Complex design
    For handle hazard

## Slide 3: Final Project
HW3: Single Cycle MIPS/RISC-V
Final Project: Pipelined MIPS/RISC-V Processor
  With Instruction cache and data cache

## Slide 4: Pipeline
Splits into several functional unit and perform instruction in parallel way
Your design should follow this 5-stage pipelined structure

## Slide 5: Required Instruction Set
You need to modify several pars to fit our specifications.
For example, you need to add the path for J-type instructions

## Slide 6: Hazards
In order to implement pipelined-MIPS, you need to resolving hazard in hardware
  Structural Hazard
    the hardware cannot support the combination of instructions
  Data Hazard
    data that is needed to execute the instruction is not yet available (dynamic).
  Load-use Data Hazard
    load instruction (lw) (read data from main memory) has not yet become available when it is requested

## Slide 7: How’s the test works?
I_mem: Instruction Memory
D_mem: Data memory
Your design

## Slide 8: Extensions (MIPS)
Branch Prediction(+define+BrPred)
  Always not branch
  Branch / Not branch / Branch
  Always branch
L2 Cache(+define+L2Cache)
  Long version of Fibonacci
Multiplication/Division (+define+MultDiv)
  Factorial

## Slide 9: Branch Prediction
For loop is commonly see in programming
  for(i=0;i<k;i++)  they did BEQ in every loop
To increase overall efficiency of system, branch prediction is always used
Waste 99 cycles
With branch prediction  waste 3 cycles

## Slide 10: Comparison Metrics
Score 1 (BP_S1): Total execution cycles of ‘I_mem_BrPred’
  BP_S1 = total cycle counts of the I_mem_BrPred
Score 2 (BP_S2): Total execution cycles of ‘I_mem_hasHazard’
  BP_S2 = total cycle counts of the I_mem
Score 3 (BP_S3): Synthesis area of BPU (um2)

## Slide 11: L2 Cache
Main goal
  Add 2 separate L2 caches for I-cache and D-cache
  Unified L2 cache (1 L2 cache for both L1 I-cache & L1 D-cache) will be considered as better design (not required)
Total size of respective L1 cache is suggested to be 32 words
  8 blocks & each 4 words
Total size of respective L2 caches(I+D) are suggested to be 256 words
  Block size and number of blocks are up to your considerations

## Slide 12: Comparison Metrics
Base on the test program: “I_mem_L2Cache”
Score 1 (L2C_S1): Avg. memory access time (ns)
  L2C_S1 = HT1 + MR1*(HT2+MR2*MP2)
  HT: hit time
  MR: miss rate
  MP: miss penalty
  ~1: of level 1 cache
  ~2: of level 2 cache
Score 2 (L2C_S2): Total execution time (ns)
  L2C_S2 = total execution time of the test program
Don’t worry about the performance evaluation. It is just one of the criteria. Focus more on what you design to solve problems you face.

## Slide 13: Multiplication/Division
Main goal
  Add a computation unit and control unit to support multiplication and division instructions

## Slide 14: Comparison Metrics
Base on the test program “I_mem_MultDiv”
Score 1 (MD_S1): Area of MultDiv (um2)
  MD_S1 = area of MultDiv - area of baseline chip
Score 2 (MD_S2): Total execution time (ns)
  MD_S2 = total execution time of test program
Score 3 (MD_S3): Minimum clock period (ns)
  MD_S3 = clock period of MIPS core
Don’t worry about the performance evaluation. It is just one of the criteria. Focus more on what you design to solve problems you face.

## Slide 15: Extensions (RISC-V)
Branch Prediction(+define+BrPred)
  Always not branch
  Branch / Not branch / Branch
  Always branch
L2 Cache(+define+L2Cache)
  Long version of Fibonacci
Supporting compressed instructions (+define+(de)compression)
  Extract C-Instructions
  PC increment
  Address alignment issues

## Slide 16: Compressed Instruction
Implement the following 16 C-instructions as the extension to your base RISC-V core
Extract information encoded in C-instructions
PC increment
Address alignment issued

## Slide 17: Comparison Metrics
A(compressed design – baseline design) *T(given compressed testbench)
Some comparison of different method can be discuss in presentation or in report

## Slide 18: Simulation Example
Change +noHazard for testing different cases
  +hasHazard
  +BrPred
  +L2Cache
  +MultDiv

## Slide 19: Grading Policy
All grades of this project consist of three equal aspects:
  1) Proposal: Project check point (5%)
  2) Presentation (45%)
  3) Final Report: technical features (50%)
The technical features are grading by two parts:
  Baseline (50%)
  Extension (50%)

## Slide 20: Baseline (50%)
The solid requirements include:
  Supporting all instructions above
  With caches
  Pass all test assembly programs
  Complete the circuit synthesis. Note that the slack cannot be negative.
Then the performance is evaluated by:
  Area (um2) * Total simulation time (ns);
And baseline points will be based on your AT ranking among other MIPS teams.

## Slide 21: Extension(50%)
There are three topics of extension.
  Branch prediction mechanism.
  Two-level caches, i.e. with L2 caches.
  Supporting multiplication and division.
Implement as much and deep as you can of the topics of extension.
Deeper exploration  higher score
  The content also affect quality of presentation

## Slide 22: Presentation Hint
More performance from deeper pipelines, parallelism (Chap. 4.10, page 332) may explore in your final project reports!
  Branch prediction
  Multiple issues
  VLIW (Very long length Instruction Word)
  Superscalar
  Dynamic scheduling
  Out-of-order execution
  Speculation
  Reorder buffer
  Register renaming

## Slide 23: ※Notice
Latches are not allowed in gate level code after synthesis, use Flip-flop instead.
Negative Slack and Timing Violations are not allowed after synthesis.
The tsmc13.v file is not allowed to be downloaded! Or you may offend the copyright protected by NTU & CIC!

## Slide 24: Find your partner and topic
Choose the topic you want to do, due 2021/05/19 24:00 (only team leader)
  https://forms.gle/krZGPGbbr7gcc2Hg7

## Slide 25: Timeline